## Slide 1
Future projection of wind and solar energy potential over China
Jia Wu
BCC/CMA
FOCRAII2024
May 10, 2024, Qingdao

## Slide 2
Outline
1
Motivation
2
Model, data and methods
3
Future projection of wind energy
4
Future projection of solar energy

## Slide 3
In the context of global warming, the development of renewable energy becomes highly desirable, as it will help to reduce the emissions of greenhouse gases in order to mitigate and adapt to climate.
In 2020, China's government pledged that carbon dioxide emissions would peak by 2030, and thereafter would achieve carbon neutrality by 2060.
The long-term goal of carbon neutrality in China involves new requirements for the development and utilization of wind and solar energy.
By 2030, the total installed capacity of wind and solar power will exceed 1.2 billion kilowatts.
Motivation

## Slide 4
However, due to data limitations, relatively little effort has been made to project future changes in wind and solar energy over different sub-regions of China.
The present study was motivated by supporting future wind and solar energy deployment at local scales.
Accordingly, we investigated seasonal change, inter-annual variability and long term change of wind and solar energy potential based on a set of high-resolution dynamical downscaling simulations under different climate scenarios.

## Slide 5: & CORDEX-CORE
CORDEX-RCMs
  Why do we need Regional Climate Downscaling?
  Bias inherited from GCMs
  High resolution demand for regional climate change
The impacts of a changing climate, and the adaptation strategies required more regional and national scales. Regional Climate Downscaling (RCD) has an important role to play by providing projections with much greater detail and more accurate representation of localised extreme events.
CORDEX (Coordinated Regional Climate Downscaling Experiment) sponsored by WCRP. The goal of CORDEX is to provide regionally downscaled climate projections for most land regions of the globe, as a compliment to CMIP5/CMIP6
  CORDEX Phase I：50km
  CORDEX Phase II：25km
  CORDEX Phase III……

## Slide 6
GCMs
(CMIP5/6)
Reanalysis data/6hr driving filed
RCP/SSPs…
Dynamical downscaling
RegCM4/5
Statistical downscaling
QM
Statistical downscaling
QM
Multi-simulations of high resolution projection dataset
~102 km
101 ~100 km
High resolution wind and solar observation datasets (CLDAS)
Downscaling Methods

## Slide 7
Model set up
Driven by multi-GCMs
  ERA-Interim
  EC-EARTH (EdR)
  MPI-ESM-MR (MdR)
  HadGEM2 (HdR)
  NorESM1-M (NdR)
  CSIRO-Mk3.6 (CdR)
Domain: CORDEX-EA (phase II), 25km resolution
Version: RegCM4.4
CLM land surface process + Emanuel convection
Updated vegetation cover over China
Updated surface emissivity
  For bare soil and snow in CLM: 0.96 and 0.97 to 0.80 and 0.92 following observation literatures
  Reduced effectively the cold bias in DJF
  Period: 1986-2100

## Slide 8
Outline
1
Motivation
2
Model, data and methods
3
Future projection of wind energy
4
Future projection of solar energy

## Slide 9
Surface wind
Solar radiation
GCMs/RCMs validation
Model evaluation based different observation resources
Wu and Shi, IJOC, 2021
Wu et al., ESS, 2022
Observational data with good quality: CN05.1, ERA5, ISCCP.
RegCM downscaling showed similar ability with CMIP6-GDDP, and the regional model has a better simulation on solar radiation than the corrected global model simulation.

## Slide 10
The COR is 0.5-0.7, the deviation is about 1-2m/s.
RCM
OBS
Bias correction
mesoscale numerical simulation
Zhu et al, 2021
bias-corrected output showd a good reliability
and applicability of the current simulations
Orig-RCM
Corrected RCMs
Bias correction for wind speed
Compared with other CORDEX-EA simulation
The COR between the original simulation and observation is less than 0.4, and the absolute deviation is basically above 2m/s.
Wu et al, ACCR, 2021.
Li et al., 2020
Notes: (It was
effectively integrated and assimilated the 2400 observation
stations and 169 sounding stations)

## Slide 11
Wind resource calculation
80 m height wind turbine
(Peterson and Hennessey, 1978)
(Manwell et al., 2009)
wind power density（WPD）
classification criteria for available wind energy resources
Zhu et al, 2021
considered the effects of annual mean wind speed and land utilization rate
variability of WPD

## Slide 12
Subregion | RCP2.6 | RCP4.5 | RCP8.5 | range
NEC | −0.31 | 0.41 | 0.45 | −0.31 ~ 0.45
NC | 0.39 | -0.29 | -0.41 | −0.41 ~ 0.39
SC | 0.18 | 0.80* | 1.10* | 0.18 ~ 1.10
NWC | −0.75* | −0.85* | −1.51* | −1.51 ~ −0.75
SWC | −0.72* | −1.72* | −2.18* | −2.18 ~ −0.72
Increase in SC
Decrease in NWC and SWC
The largest reduction existed in Tarim Basin.
2046-2065
2080-2099
low
middle
high
A decrease in annual wind power density ranged from 1.14% to 0.36% per decade among the three scenarios
Wu et al., ACCR, 2021
Trends during 2020–2099
Projected changes in WPD
Projected changes in WPD over China by the middle and late of the 21st century under different RCPs (relative to 1986-2005)

## Slide 13
The areas in different categories and their proportion of total area
In the future, the area of ‘very abundant’ , abundant, and good were projected to decrease in the future.
For low scenario, the reduction magnitude of above three types of wind resources were projected to decrease in the late 21st.
Category | Present area (104km2)/ Proportion (%) | RCP2.6 middle/late (%) | RCP4.5 middle/late (%) | RCP8.5 middle/late (%)
Very abundant | 18.4/13.3 | −25.8/3.7 | −9.7/−15.1 | −23.3/−42.8
Abundant | 37.9/27.3 | −11.6/−9.2 | −10.9/−11.2 | −10.1/−11.9
Good | 33.6/24.2 | 3.4/1.7 | −4.9/−7.1 | −1.8/−3.7
Moderate | 41.4/29.8 | 4.9/3.4 | −1.4/5.1 | 2.9/6.6
Low wind speed | 7.6/5.5 | −18.2/−15.9 | 2.3/−13.9 | −7.2/−8.8
Notes: Implying the importance of a low emissions scenario to mitigate the reduction in wind energy resource in the future.

## Slide 14
Subregion | Trend （%/10 a） | COR
SC | −0.18/−0.05/0.47* | −0.15/−0.01/0.15
NWC | −0.21/−0.52*/−0.65* | 0.15/0.23*/0.32*
SWC | −0.41*/−0.83*/−1.52* | 0.14/0.18*/0.48*
The large-scale circulation may modify the change in the wind fields and lead to a decrease in WPD over NWC and SWC.
local effects (e.g. drag forces) seem to play a more important role than large-scale circulation over SC.
SC
NWC
SWC
Mean sea level pressure
WPD
Major cause
Notes: Accordingly, we analyzed the changes in
MSLP gradient (Fig. 11) over the three sub-regions (South
China, northwestern China and southwestern China) that
showed significant change in wind energy potential
However, in South China, although significant signals of
change existed in the MSLP gradient and WPD under the
RCP8.5 scenario, no significant link ( p ＞ 0.05) between the
change in WPD and the change in MSLP gradient could be
identified.

## Slide 15
Changes in wind power generation under different emission scenarios
(%, relative to 1986-2005)
Decrease under middle and high scenarios
For low scenario, several regions show an increasing trend at the later 21st.
1
2
3
4
5
6
Wind power generation projected in the Three North region
Notes: Constructing a function between wind speed and power generation

## Slide 16
Subregion | RCP2.6 | RCP4.5 | RCP8.5
reg01 | −0.66 | −0.68 | −1.54*
reg02 | 0.07 | −0.83* | −1.50*
reg03 | −0.05 | −0.43 | −1.32*
reg04 | 1.43* | −1.91* | −0.93
reg05 | 1.55* | −0.59 | 0.13
reg06 | 1.12* | −1.14* | −1.34*
Trend(%/per decade)
A decreasing trend was found at three sub-regions under different scenarios, and the magnitude of the decrease increased as the emission concentration increased.
The power generation of the three eastern regions increased in the RCP2.6 scenario, while decreased in other scenarios.

## Slide 17
Outline
1
Motivation
2
Model, data and methods
3
Future projection of wind energy
4
Future projection of solar energy

## Slide 18
Taylor diagrams of the three downscaling simulations (HdR, MdR, and NdR) and their ensemble mean (ENS) for surface solar radiation over China
Better than wind surface simulation.
The markers were generally close to each other--consistent performance amongst the three downscaling simulations in reproducing the seasonal mean of surface solar radiation over China.
ENS showed overall reliability of model performance.
Smaller biases between the ensemble mean and ERA5.
Model evaluation based different observation resources
Notes: The red/blue markers indicate the results between the simulations and observation/ERA5.
Among the four seasons, greater overestimation
occurred in JJA between the ensemble mean and station dataset, with the largest bias (>25%) in central and
south China, which might result from the driving GCMs underestimating the summer monsoon precipitation over
these regions (Jiang et al., 2016), which would cause less cloud that is then inherited by the RCM.

## Slide 19
Overestimation in JJA was the largerest .
Added values found in RCMs.
The spatial distribution of surface solar radiation over China
MAM
JJA
SON
DJF
Wu et al., ESS, 2022
Notes: , which might result from the driving GCMs underestimating the summer monsoon precipitation

## Slide 20
The PV was calculated following the equation of Jerez et al. (2015). This equation considers the effects of radiation, temperature and wind speed. where G and GSTC is the downward solar radiation currently and under standard test conditions (1000 W m −2), respectively. PR is the performance ratio of the PV cell (Mavromatakis et al., 2010; Davy and Troccoli, 2012).
radiation
temperature
Wind speed
Solar power output from photovoltaic (PV) calculation

## Slide 21
Characterized by an increase in east and central China, and a consistent decrease in the solar-energy-abundant regions.
With more significant magnitude apparent in higher scenario.
Season | low | middle | high
MAM | −0.06 | −0.29* | −0.51*
JJA | 0.00 | −0.12 | −0.35*
SON | 0.00 | −0.05 | −0.26*
DJF | 0.02 | −0.22* | −0.62*
ANN | −0.03 | −0.16* | −0.42*
The trends of PV over China by 2020–2099
regional mean trends
low
middle
high
MAM
JJA
SON
DJF
Notes: characterized by a significant increase
(>0.2% decade −1) over north, central, and east China under RCP2.6 in all seasons, a significant decrease (ranging
from −0.2 to −0.8% decade −1) over the Tibetan Plateau under RCP4.5 in all seasons, and a significant decrease
(<–0.4% decade −1) over the Tibetan Plateau and northeast China and a significant increase in central and east
China under RCP8.5, albeit with relatively larger magnitude compared to surface solar radiation. In addition,
although consistent trends were projected under RCP4.5 and RCP8.5, an enhanced increase and decrease were
evident under the RCP8.5 scenario. Again, JJA showed different trends among scenarios; under RCP4.5 it was
north China that showed an increasing trend, whereas under RCP8.5 it was northeast China.

## Slide 22
Regional mean
region | MAM | JJA | SON | DJF
NEC | 97/3/−2 | 42/13/37 | 93/1/1 | 115/21/−36
Tibet | 47/−13/72 | 38/−1/73 | 64/3/40 | 53/−1/50
NWC | 81/1/19 | 80/−3/23 | 120/−12/−3 | 90/−12/19
Effect factor:
Contributions of radiation/temperature/wind speed
Wu et al., 2022; 2023.
low
middle
high
2021-2040
2046-2065
The Changes of PV over China during different periods
Similar pattern during different future periods
Decline in the future PV potential over most of subregions of China due to reduced radiation and increased temperature, but for the decrease over Tibetan Plateau the reduced wind speed also act as an important factor.
Notes: 对未来不同RCP情景下中国光伏发电量变化及影响因素分析结果表明， 未来中高排放情景下，我国中东部及西南地区的光伏发电量增加，而主要的太阳能丰富区如东北和西北等地区则表现为减少，这种增加和减少的幅度都随排放浓度的增加而增大，此外，春季和冬季减少幅度相对较大。但总体来看，太阳能资源的减少幅度在±5%之间，对未来的开发利用没有实质性影响。进一步对不同区域太阳能资源变化的主要影响因素进行分析发现，辐射减少和气温升高是未来光伏潜力下降的主因，但青藏高原地区，风速下降也是一个重要因素。

## Slide 23
RCM
CLDAS
Quantile mapping
6.25 km
cumulative distribution
function
Combined Dynamical and Statistical Downscaling
Downscaling system based on CLDAS, RCM projection data, and quantile mapping.
Climate Service：
climate change research report
decision consulting reports
provincial-level climate change research
Impact assessment of the energy and power industry

## Slide 24
Although the projected decrease in annual WPD and PV over abundant regions of wind and solar energy, we believe that, considering the strong inter-annual variability and uncertainty involved, these changes would not substantially affect China's future wind and solar energy plans.
Also of note was that a low emission scenario could to some extent mitigate the reduction in wind and solar energy potential in the future.
Furthermore, an increasing trend was found in wind and solar energy over central and southern China.
Conclusion

## Slide 25
Thank you！
CMIP6 driving RegCM5（18-5km）--working）